## Slide 1
Thank you for downloading our
LIFT ENTRAPMENT SOP

## Slide 2
CONTENTS
Introduction
Lift Entrapment SOP
About SIRV
Disclaimer

## Slide 3
INTRODUCTION
Working with our community we’ve put together some SOPs for you to use, free of charge.
The SOPs are designed to be read by the individual on the ground and follow the format used by our decision support system, a decision tree that asks one question and provides one or more answers and instructions.

## Slide 4
LIFT ENTRAPMENT SOP

## Slide 5
Page 1
QUESTION: Is a person currently trapped in the lift?
ANSWER: Yes.
INSTRUCTION: go to page 2

## Slide 6
Page 2
INSTRUCTION: When dealing with the occupants, the only release methods that can be tried are:
Ask the passenger to press the ground floor button and wait to see if the lift responds.
Ask the passenger to press the door open button and see if the doors will open.
NOTE: If the lift is not at floor level, NEVER suggest that the passenger gets out of the lift.
NOTE: Under NO circumstances should operators advise passengers to manually attempt to open the door or take any other course of action.
CONT…..

## Slide 7
Page 3
QUESTION: Please confirm the above instructions have been followed
ANSWER: Yes.
INSTRUCTION: go to page 4

## Slide 8
Page 4
INSTRUCTION: Ask the passengers the following questions:
Location of lift and what floors they are between?
Number of people in the lift?
Do any of the passengers have a medical condition?
Are any of the passengers distressed?
CONT…..

## Slide 9
Page 5
QUESTION: How are the passenger(s)?
ANSWER 1) Distressed and/or with a medical condition (go to page 6a)
ANSWER 2) Not distressed and/or without a medical condition (go to page 6b)

## Slide 10
Page 6a
INSTRUCTION: Follow next four steps in sequence
Contact Fire Brigade
Telephone emergency services on 999 and instruct them to attend owing to a person trapped in a lift with a medical condition or in a distressed state.
2) Contact Lift Company
Telephone lift company and instruct them to attend owing to a person trapped in a lift with a medical condition or in a distressed state. Confirm an estimated time of arrival on site.
3) Use the following as advice for any questions asked (go to page 7)
CONT…..

## Slide 11
Page 6b
INSTRUCTION: Follow next three steps in sequence
1) Contact Lift Company
Telephone lift company and instruct them to attend owing to a person trapped in a lift with a medical condition or in a distressed state. Confirm an estimated time of arrival on site.
2) Use the following as advice for any questions asked (go to page 7)
CONT…..

## Slide 12
Page 7
QUESTION | SUGGESTED ANSWER
"The lift is going to fall!" | "I understand your fears, but the lift/elevator has many safety devices to help stop the lift from falling. Please try and make yourself comfortable, we have called the lift company and they will be here as soon as possible. "
"There is no air!” ”Is there any air in the lift when I am trapped” | "I can reassure you - the elevator has plenty of ventilation. There is more air closer to the floor; you may wish to sit on the floor to make yourself more comfortable."
CONT…..

## Slide 13
Page 8
QUESTION | SUGGESTED ANSWER
"I am going to be sick!" | "Please make yourself as comfortable as possible. I can reassure you, we are working to get you out as soon as we can.
"I am claustrophobic!" | "I understand your fears, I can reassure you, we are working to get you out: it would help you if you sat on the floor as there is more air closer to the ground.”
CONT…..

## Slide 14
Page 9
QUESTION | SUGGESTED ANSWER
"Can I make a phone call from here?" | "From the lift phone, you can only call us. If you have a mobile phone and coverage, you can call someone or I would be more than happy to call on your behalf. Would you like me to call someone on your behalf?"
"Can I just force the doors open?" | "Please do not force the doors open. The lift might restart and you will risk injuring yourself. Please wait for the mechanic to arrive.”
CONT…..

## Slide 15
Page 10
QUESTION | SUGGESTED ANSWER
"I am in a hurry for an important meeting!" | "I can call someone on your behalf. Is there any one we can call for you, to let them know where you are?"
"Can you make the lift go to my floor?” | “If the lift has stopped, unfortunately no, as I cannot operate the lift, but have you tried pressing the ground floor button? If the lift is not taking you to your floor, you will need to speak to either onsite security or other staff”
CONT…..

## Slide 16
Page 11
INSTRUCTION: 3) & 4) Complete the following incident form to record the lift entrapment (suggested form fields shown below)
Date & Time | Any medical conditions
Site & Location | Any passengers distressed
Floor (or between floors) | Passenger tel. no’s
Reason for entrapment | Comments
Names of people trapped | Images
CONT…..

## Slide 17
Page 12
No. of people trapped | Lift number
Contractor contacted | Fire Brigade contacted
Time contractor contacted | Fire Brigade contacted at what time
Time contractor expected | Sketch (if applicable)

## Slide 18
ABOUT SIRV
Systematic Intelligent Risk Valuation (SIRV), is a software platform used by some of the biggest brands in the world to improve the quality of reporting and decision making.
Find out more at getsirv.com
Got any feedback? We’d love to hear your thoughts, please email info@sirv.co.uk

## Slide 19
DISCLAIMER
The information contained in this website is for general information purposes only. The information is provided by SIRV Systems Limited and while we endeavour to keep the information up to date and correct, we make no representations or warranties of any kind, express or implied, about the completeness, accuracy, reliability, suitability or availability with respect to the website or the information, products, services, or related graphics contained on the website for any purpose. Any reliance you place on such information is therefore strictly at your own risk.
In no event will we be liable for any loss or damage including without limitation, indirect or consequential loss or damage, or any loss or damage whatsoever arising from loss of data or profits arising out of, or in connection with, the use of this website.
Through this website you are able to link to other websites which are not under the control of SIRV Systems Limited. We have no control over the nature, content and availability of those sites. The inclusion of any links does not necessarily imply a recommendation or endorse the views expressed within them.
Every effort is made to keep the website up and running smoothly. However, SIRV Systems Limited takes no responsibility for, and will not be liable for, the website being temporarily unavailable due to technical issues beyond our control.